## Slide 1: OVERALL EQUIPMENT EFFICIENCY
Principles, Applications, and Analysis

## Slide 2: —Peter Drucker/William Thomson “You can not improve what you can not measure”

## Slide 3: Table of contents 01 Understanding OEE History and Definition 02 OEE as a Business Tool Benefits of using OEE 03 OEE Calculation OEE Components 04 OEE as a driver for Improvement Analysis, Improvement

## Slide 4: Understanding OEE 01

## Slide 5: History of OEE
The concept of OEE -Overall Equipment Effectiveness was written about by Seiichi Nakajima in 1989
Notes: Seiichi Nakajima is from Japan Institute of Plant Maintenance
TPM Development Program was translated from Japanese book TPM Tenkai published in 1982
OEE was first described –as a central component of the TPM methodology- in Seiichi Nakajima’s book ‘TPM tenkai’ (1982, JIPM Tokyo).
By the end of the 1980’s, the concept of TPM became more widely known in the Western world. At the time, Productivity Press (OR, USA) published English translations of two books by JIPM expert Seiichi Nakajima: Introduction to TPM and TPM Development Program.

## Slide 6: History of OEE
SEMATECH (US)
Semiconductor Manufacturing Productivity OEE Guidebook
1995
Fuji (Holland)
Largest investment
outside of Japan
3 factories
Zero Defects, Zero Loss
1980s
OEE Benchmarking
Present
Arno Koch (US)
OEE Toolkit
OEE for Operators
End of 1990s
Notes: 1. Around the same time, in Europe, Fuji Photo-Film made the largest investment ever done outside of Japan so far, building 3 factories in Holland. The challenge for the factory management:
“Producing Zero Defect and Zero Loss, using Japanese principles in a Western environment”.
Fuji’s Director Steven Blom resumes:
“Measure OEE and eliminate the losses, using Small Group Activities”.
Around 1995, in the semiconductor industry SEMATECH publishes its ‘Semiconductor Manufacturing Productivity Overall Equipment Effectiveness (OEE) Guidebook‘ with guidelines for OEE implementation is semiconductor manufacturing.
At the end of the ’90s, Arno Koch worked closely together with the editors and authors of Productivity Press, publishing ‘OEE Toolkit’ (the predecessor of OEE Coach) and ‘OEE for Operators’ (part of the Shingo Prize winning shopfloor series).
This effectively made OEE accessible and feasible for many Western companies’ production departments.
OEE Industry Standard (Holland)
On request of several OEE-using multinationals, Koch initiated in 2001 the “OEE Industry Standard Endeavour” that resulted in the OEE Industry Standard, since then offering OEE definitions and -standards to manufacturers around the globe. (see: OEE Industry Standard)
Hansen (US)
In the same year 2001 Bob Hansen wrote his book “Overall Equipment Effectiveness” attempting to clarify the steep learning curve to use OEE effectively with emphasis on maintenance and reliability.
CETPM (Germany)
In 2006 In Germany, at the Ansbach University of Applied Technology, Prof. Dr. Constantin May starts the Centre of Excellence for TPM (CETPM). OEE courses become a standard in its curriculum; in the TPM-instructor course, instructors are now systematically trained how to apply OEE.
Meanwhile OEE is being used worldwide in virtually every kind of production-process thinkable.
The experience gained by applying OEE to a vast number of incredibly diverse machines and equipment both in batch processes and discrete industries throughout the entire world, subsequently ensured that these ‘interesting theories’ were modeled into the practical tools that you will read about on this site.
Koch (Holland – Germany)
After writing “OEE Toolkit” (1995) and co-creating “OEE for operators” (1999), the vast amount of implementation insights gained so far, result in a “complete OEE user guide”, first written by Arno Koch in 2007, updated in 2015, titled; “OEE for the Production Team”, available in English and Dutch, in German since 2008 and in Portuguese since 2013.

## Slide 7: History of OEE
Why was OEE needed in the
first place?
Notes: 1. Around the same time, in Europe, Fuji Photo-Film made the largest investment ever done outside of Japan so far, building 3 factories in Holland. The challenge for the factory management:
“Producing Zero Defect and Zero Loss, using Japanese principles in a Western environment”.
Fuji’s Director Steven Blom resumes:
“Measure OEE and eliminate the losses, using Small Group Activities”.
Around 1995, in the semiconductor industry SEMATECH publishes its ‘Semiconductor Manufacturing Productivity Overall Equipment Effectiveness (OEE) Guidebook‘ with guidelines for OEE implementation is semiconductor manufacturing.
At the end of the ’90s, Arno Koch worked closely together with the editors and authors of Productivity Press, publishing ‘OEE Toolkit’ (the predecessor of OEE Coach) and ‘OEE for Operators’ (part of the Shingo Prize winning shopfloor series).
This effectively made OEE accessible and feasible for many Western companies’ production departments.
OEE Industry Standard (Holland)
On request of several OEE-using multinationals, Koch initiated in 2001 the “OEE Industry Standard Endeavour” that resulted in the OEE Industry Standard, since then offering OEE definitions and -standards to manufacturers around the globe. (see: OEE Industry Standard)
Hansen (US)
In the same year 2001 Bob Hansen wrote his book “Overall Equipment Effectiveness” attempting to clarify the steep learning curve to use OEE effectively with emphasis on maintenance and reliability.
CETPM (Germany)
In 2006 In Germany, at the Ansbach University of Applied Technology, Prof. Dr. Constantin May starts the Centre of Excellence for TPM (CETPM). OEE courses become a standard in its curriculum; in the TPM-instructor course, instructors are now systematically trained how to apply OEE.
Meanwhile OEE is being used worldwide in virtually every kind of production-process thinkable.
The experience gained by applying OEE to a vast number of incredibly diverse machines and equipment both in batch processes and discrete industries throughout the entire world, subsequently ensured that these ‘interesting theories’ were modeled into the practical tools that you will read about on this site.
Koch (Holland – Germany)
After writing “OEE Toolkit” (1995) and co-creating “OEE for operators” (1999), the vast amount of implementation insights gained so far, result in a “complete OEE user guide”, first written by Arno Koch in 2007, updated in 2015, titled; “OEE for the Production Team”, available in English and Dutch, in German since 2008 and in Portuguese since 2013.

## Slide 8: History of OEE
RUNS 90 HRS | STOPS 10 HRS
Situation A – 10 hr breakdown, after every 90 hrs
Total: 100 hrs
Situation B – 1 hr breakdown, every 9 hrs
Total: 100 hrs
Notes: 1. Around the same time, in Europe, Fuji Photo-Film made the largest investment ever done outside of Japan so far, building 3 factories in Holland. The challenge for the factory management:
“Producing Zero Defect and Zero Loss, using Japanese principles in a Western environment”.
Fuji’s Director Steven Blom resumes:
“Measure OEE and eliminate the losses, using Small Group Activities”.
Around 1995, in the semiconductor industry SEMATECH publishes its ‘Semiconductor Manufacturing Productivity Overall Equipment Effectiveness (OEE) Guidebook‘ with guidelines for OEE implementation is semiconductor manufacturing.
At the end of the ’90s, Arno Koch worked closely together with the editors and authors of Productivity Press, publishing ‘OEE Toolkit’ (the predecessor of OEE Coach) and ‘OEE for Operators’ (part of the Shingo Prize winning shopfloor series).
This effectively made OEE accessible and feasible for many Western companies’ production departments.
OEE Industry Standard (Holland)
On request of several OEE-using multinationals, Koch initiated in 2001 the “OEE Industry Standard Endeavour” that resulted in the OEE Industry Standard, since then offering OEE definitions and -standards to manufacturers around the globe. (see: OEE Industry Standard)
Hansen (US)
In the same year 2001 Bob Hansen wrote his book “Overall Equipment Effectiveness” attempting to clarify the steep learning curve to use OEE effectively with emphasis on maintenance and reliability.
CETPM (Germany)
In 2006 In Germany, at the Ansbach University of Applied Technology, Prof. Dr. Constantin May starts the Centre of Excellence for TPM (CETPM). OEE courses become a standard in its curriculum; in the TPM-instructor course, instructors are now systematically trained how to apply OEE.
Meanwhile OEE is being used worldwide in virtually every kind of production-process thinkable.
The experience gained by applying OEE to a vast number of incredibly diverse machines and equipment both in batch processes and discrete industries throughout the entire world, subsequently ensured that these ‘interesting theories’ were modeled into the practical tools that you will read about on this site.
Koch (Holland – Germany)
After writing “OEE Toolkit” (1995) and co-creating “OEE for operators” (1999), the vast amount of implementation insights gained so far, result in a “complete OEE user guide”, first written by Arno Koch in 2007, updated in 2015, titled; “OEE for the Production Team”, available in English and Dutch, in German since 2008 and in Portuguese since 2013.

## Slide 9: What is OEE
OEE (Overall Equipment Effectiveness) is both a process monitoring and process improvement tool
A framework of measuring the efficiency of a process, line, or machine

## Slide 10: What is OEE
A “best practices” way to continuously improve the effectiveness of manufacturing processes

## Slide 11: What is OEE
Takes into account the most common losses, and narrows them down into metrics that provide excellent gauge for measuring where you are – and how you can improve

## Slide 12: What is OEE
Takes into account the most common losses, and narrows them down into metrics that provide excellent gauge for measuring where you are – and how you can improve

## Slide 13: OEE as a Business Tool 02

## Slide 14: Why use OEE
It helps us to see and understand the current process and system status.
It facilitates in making our improvement plans
It helps us measure our performance

## Slide 15: Why use OEE

## Slide 16: Why use OEE

## Slide 17: Why use OEE
Notes: COST REDUCTION – remain competitive in the market

## Slide 18: Why use OEE
Notes: GROWTH – expansion capabilities

## Slide 19: Why use OEE
Notes: Profit maximization - Capital is used as effectively as possible

## Slide 20: Why use OEE
Notes: Process Optimization and Improvement – line balancing, manpower utilization, energy consumption, yield improvement, output and capacity increase

## Slide 21: Why use OEE
Notes: Risk Minimization -- Identify and minimize production risks, failure risks

## Slide 22: Why use OEE
Notes: Solve problem to root cause -- Reducing fire fighting, analyzing problems and eliminating them sustainably

## Slide 23: OEE Calculation 03
58%
42%

## Slide 24: OEE COMPONENTS
Availability accounts for when the process is not running both Unplanned Stops and Planned Stops.
Notes: Solve problem to root cause -- Reducing fire fighting, analyzing problems and eliminating them sustainably

## Slide 25: OEE COMPONENTS
Performance accounts for when the process is running slower than its theoretical top speed.
Notes: Performance accounts for when the process is running slower than its theoretical top speed.

## Slide 26: OEE COMPONENTS
Quality accounts for manufactured parts that do not meet set quality standards
Notes: Quality accounts for manufactured parts that do not meet set quality standards.

## Slide 27: OEE CALCULATION
Notes: Quality accounts for manufactured parts that do not meet set quality standards.

## Slide 28: OEE as a driver for improvement 04

## Slide 29: OEE ANALYSIS
Notes: Quality accounts for manufactured parts that do not meet set quality standards.

## Slide 30: OEE ANALYSIS
Notes: Quality accounts for manufactured parts that do not meet set quality standards.

## Slide 31: OEE ANALYSIS
Notes: Quality accounts for manufactured parts that do not meet set quality standards.

## Slide 32: OEE ANALYSIS
Notes: Quality accounts for manufactured parts that do not meet set quality standards.

## Slide 33: OEE ANALYSIS
Notes: Quality accounts for manufactured parts that do not meet set quality standards.

## Slide 34: OEE IMPROVEMENT
Notes: Quality accounts for manufactured parts that do not meet set quality standards.

## Slide 35: OEE IMPROVEMENT
Notes: Quality accounts for manufactured parts that do not meet set quality standards.

## Slide 36: OEE IMPROVEMENT
Notes: Quality accounts for manufactured parts that do not meet set quality standards.

## Slide 37: OEE IMPROVEMENT
Notes: Quality accounts for manufactured parts that do not meet set quality standards.

## Slide 38: OEE IMPROVEMENT
Notes: Quality accounts for manufactured parts that do not meet set quality standards.

## Slide 39: OEE FINAL REMINDERS!
Notes: Quality accounts for manufactured parts that do not meet set quality standards.

## Slide 40
Notes: Quality accounts for manufactured parts that do not meet set quality standards.

## Slide 41
Notes: Quality accounts for manufactured parts that do not meet set quality standards.

## Slide 42: MARK ANTHONY CARO
mdcaro@up.edu.ph
Project Management
Engineering and Maintenance
TPM
Lean Manufacturing
Energy/Environment/Quality Management